## Slide 1: A Novel Breeding Program for the Domestication of Lemnaceae and The Production of Fuel Butanol
March 6th, 2025

## Slide 2
We are Interested in Turning Duckweed into a Crop and Using it To Produce Butanol
Lemnature Aquafarms
Weed
Crop
NC Dept. Ag
Fuel Butanol
Pigs
Bioenergy Research Initiative
Jay Cheng
Hannah Wall

## Slide 3
Crop Attributes:
High Yielding
as much as 12 (MT/acre/year)
High Quality Biomass
As high as 35% protein
As high As 20% starch
Grows Well on Waste
Grows well on any wastewater
Hyperaccumulates nutrients
[Parabel]
Sustainable Ag Systems:
Closed Loop Nutrient
Reuse
Growing More Biomass
on Less Land
Bioproducts
The Lemnaceae are a Family of Plants with Great Agricultural Potential
Why will Lemna make a good crop?

## Slide 4
Lemna Has Potential to Be More Sustainable Than Our Current Crops
Greenhouse Gas Emissions
Nutrient Management
CO2
N2O
CH4
N
7
Nitrogen
P
15
Phosphorus
K
19
Potassium
Land Use
~45%
Why will Lemna make a good crop?

## Slide 5
Breeding is Required for Any Plant or Animal to Reach it’s Full Potential
How do we turn a weed into a crop?
All crops have been significantly improved over the past ~80 years
Yield (Dry tons/acre/year)
Current Yield
Theoretical Yield

## Slide 6: Traits of Interest are Similar to Other Crops
- Heat tolerance
- Biomass composition (increase starch/Fat content)
- Density tolerance (this is where most of the yield gains in corn have come from)
How do we turn a weed into a crop?

## Slide 7: Selective Breeding is The Basis of Crop Improvement
How do we turn a weed into a crop?
Select Top 30
Random Mating
New Population
Phenotype
300 Lines

## Slide 8
How do we turn a weed into a crop?
Crossing Pollinating Is Essential For Breeding
* This is also very useful or essential for basic genetic or quantitative genetic studies.
Shaking Promotes Pollination
Seed-to-seed in 5-7 weeks!
Seeds Form and Sink to the Bottom
Initiate Flowering
[Fourounjian P, Slovin J, Messing J. Int J Mol Sci . 2021]
Germinated Seeds Float to the Surface and Grow into New Varieties
SEM Image: Josh Strable
Alex Aragon Raygoza
(NCSU Biochemistry)

## Slide 9
Phenotyping Requires a Tradeoff Between Accuracy and Throughput
How do we turn a weed into a crop?
1000 Varieties / Month
100 Varieties / Month
6 Varieties / Year
High Throughput (Image-based)
Medium Throughput (Mass measurements)
Low Throughput (Field trials)

## Slide 10
A
B
C
D
E
Automated Lab-scale PHenotyping Apparatus (ALPHA)
How do we turn a weed into a crop?
Victoria Augoustides
Kassidy Robinson
Notes: In order to breed fast, we need to be able to phenotype fast. This is a lab-based phenotyping system that is able to very quickly (within a few weeks) screen through hundreds of different varieties and determine the best ones.

## Slide 11
Automated Lab-scale PHenotyping Apparatus (ALPHA)
How do we turn a weed into a crop?
Notes: In order to breed fast, we need to be able to phenotype fast. This is a lab-based phenotyping system that is able to very quickly (within a few weeks) screen through hundreds of different varieties and determine the best ones.

## Slide 12
How do we turn a weed into a crop?
Using Image Processing, Pictures are Turned into Growth Curves
Kassidy Robinson

## Slide 13
How do we turn a weed into a crop?
Using Image Processing, Pictures are Turned into Growth Curves
Germany Clone
France Clone
France Clone
Germany Clone
Kassidy Robinson

## Slide 14
Selection on The ALPHA System Works
Current Projects
Kassidy Robinson
NC Water Resources Research Institute
Mike Burchell
François Birgand
Praveen Kolar
Liz Riedel (M.S. Student)

## Slide 15
Greenhouse-scale Automated Mass Measurement Apparatus (GAMMA)
How do we turn a weed into a crop?
Mike Adcock
Kassidy Robinson
Load Cell (Mass Sensor)
Hydroponic Grow Basket
Arduino Microcontroller

## Slide 16
Greenhouse-scale Automated Mass Measurement Apparatus (GAMMA)
Mike Adcock
Kassidy Robinson
How do we turn a weed into a crop?
GAMMA Growth Curves

## Slide 17
Outdoor-cultivation Mass Evaluation and Growth Apparatus (OMEGA)
How do we turn a weed into a crop?

## Slide 18
Leman Can Be Used to Make Biofuel
Current Project
Jay Cheng
Mike Adcock
Hannah Wall (M.S.)
NC Dept. Ag
Pigs
Storage Lagoon
Lemna Cultivation
Fuel Butanol

## Slide 19
Past Projects
Lemna Can Be Used to Make Ethanol
- Lemnaceae can produce 50% more ethanol / hectare than the average U.S. corn crop.
[Xu J, Cui W, Cheng JJ, Stomp A. Biosyst Eng. 2011]
Jay Cheng
(NCSU, BAE Department)
Corn
- 10s of $Billions in variety development
-Fertilizer
-herbicides
-pesticides
Duckweed
- swine waste
Inputs

## Slide 20
Leman Can Be Used to Make Biogas
Past Projects
Jay Cheng
Joe Sagues
Mike Adcock
Lily Lower (M.S.)
NC Dept. Ag

## Slide 21
Lemna Can Be Adapted to Grow Better on Hog Wastewater
Current Project
2-3 Cycles of Recurrent Selection (ALPHA)
One more round of selection (GAMMA)
Field Trials on 6 Varieties (OMEGA)
Fuel Butanol
Pigs

## Slide 22
Butanol can Be Fermented from Biomass
Current Project
Jay Cheng
Mike Adcock
Hannah Wall (M.S.)
NC Dept. Ag

## Slide 23
Butanol is a Future Biofuel With Potential
Current Project
Jay Cheng
Mike Adcock
Hannah Wall (M.S.)
NC Dept. Ag
Fuel Butanol
Butanol is a drop-in replacement for gasoline
- It Can be used with any existing gasoline engine and blended at a higher ratio than ethanol
- It does not absorb water
- It has an energy density that is 49% higher than ethanol
Butanol - 29.2 MJ/L
Ethanol - 19.6 MJ/L
- However, it is more expensive to produce. Most of this (80%) is from feedstock cost.

## Slide 24: THANK YOU!
LIFT LAB (Lemna Improvement and Functional Transcriptomics)
- Kassidy Robinson
- Mike Adcock
- Christina Sachs
- Hannah Wall
- Bob McCann
- Kyle Curley
- Varun Govindarajan
- Victoria Augoustides
(past member)
Collaborators:
Jay Cheng
Mike Burchell
François Birgand
Praveen Kolar
Lily Lower
Liz Riedel
Colleen Doherty
Kanjana Laosuntisuk
Josh Strable
Alex Raygoza
Bioenergy Research Initiative
Project Number: 24-047-4001